## Slide 1
Noise Reduction in Communication Signals Using Deep Neural Networks
DIGITAL SIGNAL PROCESSING
MACHINE LEARNING
Exploring Deep Learning techniques to enhance signal quality by removing Gaussian noise from composite sinusoidal signals.
AAKASH GANGOTRI 1032240115
ABEER CHOUDAHA 1032233636

## Slide 2
The Challenge
Real-World Signal Corruption
Transmitted signals face inevitable corruption from thermal sources, interference, and channel degradation. Recovering the original clean signal is critical for data integrity.
Traditional filters are computationally cheap but struggle to preserve high-frequency details or adapt to complex noise patterns.

## Slide 3
Project Objectives
01
Generate Synthetic Signal
Create composite signal representing communication waveform
02
Simulate Noisy Channel
Introduce Gaussian White Noise to test conditions
03
Implement DNN
Train sequential Deep Neural Network for noise suppression
04
Benchmark Performance
Compare DNN results with Moving Average filter

## Slide 4
Signal Generation & Noise Addition
Clean Signal Composition
Synthetic signal composed of two distinct frequencies (5 Hz and 12 Hz) simulating complex waveform:
Gaussian noise added with standard deviation σ:

## Slide 5
Two Approaches Compared
Moving Average Filter
Traditional Method
Window size: 5. Averages signal points within sliding window to smooth fluctuations. Fast and simple but degrades high-frequency components.
Deep Neural Network
Proposed Method
Feed-forward DNN learns regression map predicting clean amplitude from noisy input. Leverages non-linear ReLU activation for complex pattern recognition.

## Slide 6
DNN Model Architecture
Input Layer
Receives noisy signal amplitude
Hidden Layer 1
64 neurons, ReLU activation
Hidden Layer 2
64 neurons, ReLU activation
Output Layer
1 neuron, linear activation
Training Configuration: Adam optimizer, MSE loss function, 100 epochs

## Slide 7
Performance Metrics
Mean Squared Error (MSE)
Measures average squared difference between estimated and actual values. Lower is better.
Signal-to-Noise Ratio (SNR)
Ratio of signal power to noise power, expressed in decibels (dB). Higher is better.

## Slide 8
Experimental Results
Low Noise
Low Fidelity
High Noise
High Fidelity
Moving Average — Smoothed with Phase Lag
DNN Denoised — Reconstructed, Peaks Preserved
Noisy Signal — Gaussian Distorted Wave
Clean Signal — Ideal Dual-Frequency Wave
The DNN successfully reconstructed the wave shape, preserving peaks better than the moving average while the MA filter exhibited phase lag and attenuation of high-frequency components.

## Slide 9
Quantitative Performance Comparison
Metric
Input (Noisy)
Moving Average
DNN
SNR (dB)
Low
Moderate
High
MSE
N/A
Moderate
Low
The DNN approach showed higher output SNR and lower MSE, indicating successful learning to distinguish signal patterns from stochastic noise.
Key Finding
Training loss curve demonstrated effective MSE minimization over 100 epochs, indicating successful convergence without significant overfitting.

## Slide 11
Conclusion & Future Scope
Project Success
Deep Neural Networks successfully demonstrated superior signal denoising compared to traditional Moving Average filters. The DNN learned to distinguish underlying signal patterns from noise, providing robust reconstruction.
Future Directions
Implement RNN/LSTM for time-series advantages
Optimize for real-time embedded device deployment
Extend to audio and voice signal denoising